## Slide 1
قالب دستور ها به صورت 8 بیتی:
X0 X1 X2 X3 X4 X5 X6 X7
Op-Code
Operation | Op-Code
Load | 00
ALU | 01
JMP | 10
Call | 11
Instruction Name | Arguments | Instruction (Binary) | Description
Define name value | Name: name of variable or label of address |  | Define variable. Should be in first of code.
Ld_Input reg | A: Destination Reg A: Destination Reg | 0000AAXX | Directly puts input to selected reg.
Ld_Sram reg name |  | 0001AAXX | CPU Reads next word of memory to fetch Address.
LDOutput |  | 001XXXXX | Load output reg by current ALU out.
Add a¦b c¦d shl | A: In1=A?regB:regA B: In2=B?regD:regC C: Shl ALU Out if true | 01000ABC | ALU immediately write in Alu_Out. After a clock, value of regBuff fills by alu_out. By set Argument that specified by ‘C’, regBuff fill by alu_out<<1.
Sub a¦b c¦d shl |  | 01001ABC | 
In1 a¦b c¦d shl |  | 01010ABC | 
In2 a¦b c¦d shl |  | 01011ABC | 
And a¦b c¦d shl |  | 01100ABC | 
Or a¦b c¦d shl |  | 01101ABC | 
Xor a¦b c¦d shl |  | 01110ABC | 
Shl a¦b c¦d shl |  | 01111ABC | 
Jmp dir¦ind address | A: Direct if is True | 100AXXXX | Jump to address with no conditions. Destination address is in next memory block.
Jz dir¦ind address |  | 101AXXXX | Jump to address if alu zero flag is set.